Sample Coverage Chart for Cellulose and Fiberglass Insulation

Blown Cellulose “Cocoontm”  (25lb. bag)

| Thickness | R-Value | Density/ft3 | Weight/ft2. | Bags/1000ft2 | Coverage |
| --- | --- | --- | --- | --- | --- |
| 2X4 | 13 | 2.6 lbs | .75 lbs. | 28 | 36 ft2 |
| 2X6 | 20 | 2.6 lbs. | 1.192 lbs. | 43 | 23 ft2 |

Blown Fiberglass CertainTeed “Optima” (27lb. bag)

| Thickness | R-Value | Density/ft3. | Weight/ft2 | Bags/1000ft2 | Coverage |
| --- | --- | --- | --- | --- | --- |
| 2X4 | 14 | 1.6 lbs | .46 lbs. | 16.7 | 60 ft2 |
| 2X6 | 22 | 1.6 lbs | .73 lbs. | 26 | 38 ft2. |